## Slide 1: Operational systems for conjunctive water management with MAR during droughts
11212698-002
Kick-off

## Slide 2: Conceptual model
Bron: Igor Jellema (visie Vitens; in ontwikkeling)

## Slide 3: Optimization for reservoirs
Inequality constraints:
Groundwater volume physical range
  minimum and maximum water level
  pipeline capacity
  Groundwater extraction
Objective function terms:
Groundwater level operational range and target
River intake limits
Minimize river intake from the river
Boundary conditions:
Natural groundwater recharge (source/sink)
Drinking water extraction (source/sink)
Groundwater (base) flow (Darcy leakage function)
Equations (equality constraints):
: Volume
: Time
: Discharge
Schematization (conceptual model):
Optimization task: Find out when to pump how much water from the river to ensure that the water extraction can be maintained.
This is a water balance model,
not a groundwater model!
Groundwater
reservoir
Artificial recharge (river intake)
Natural groundwater recharge
Drinking water extraction
GW flow
River-aquifer interaction

## Slide 4: Priority on groundwater level
Groundwater operational range met
River intake macimum during the summer exceeded

## Slide 5: Priority on river intake
Groundwater operational range exceeded
River intake maximum during the summer obeyed
Less flow from aquifer to the river (base flow) during the summer

## Slide 6: Compromised solution – same priority
Groundwater level and river intake goal are optimized together
  same priority
  Weighting factor
    River inteake: 60%
    Groundwater level range: 40%
Groundwater operational range exceeded
River intake maximum during the summer exceeded
Tuning the weighting factors is a bit tedious

## Slide 7: Optimization model for groundwater reservoirs
Water balance model
  no groundwater flow modelled
  Darcy equation for river-aquifer interaction
Mathematical optimization
  Comes with mathematical restrictions (linear equations)
  fast solution, global optimum
Conflict resolution between use functions
  Goal programming with priorities (multiple optimizations in a sequence)
  Weighting factors for compromised solutions
Software: RTC-Tools (real-time-control tools)
  Used for pump operations, hydropower scheduling and reservoir operation (“stuwmeren”)
  Open Source, developed by Deltares, hosted under the Linux Foundation

## Slide 8: Goal programming for conflict resolution
Multiple optimizations in the sequence of prioirities
Achieved goals are maintained in consecutive optimization

## Slide 9: Strategic hearts
Bron: Igor Jellema (visie Vitens; in ontwikkeling)

## Slide 10: Strategic hearts
Bron: Igor Jellema (visie Vitens; in ontwikkeling)